## Slide 1: Environment Optimization for Crowd Evacuation
By
Glen Berseth1, Muhammad Usman2, Brandon Haworth2, Mubbasir Kapadia3, Petros Faloutsos2
University of British Columbia1, York University2, Rutgers University3
Notes: Have 30 minutes for talk? 25 minutes for presentation 5 minutes for question.

## Slide 2: Crowd Dynamics are Complex
Architects produce functional pieces of art
  Want understanding of effect of building changes
  Configuration space is infinite
  Optimal configuration for crowd dynamics
Crowd dynamics are complex
  Designers can’t predict effects of objects
  Need computation method for analysis
Notes: When designing buildings architects produce functional pieces of art that humans and in future robots have to navigate in.
  It is difficult to understand the resulting dynamic changes in a crowd due to alterations to environment geometry. A greater understanding of these changes would be of value to the game development, robotics and urban simulation communities.
  One reason for the complexity in this understanding is the infinite number of possible configurations in design space for a building
  It can be impractical even for experts to construct environments that are optimal for the dynamics of the intended occupants.
Predicting the effect of geometry changes on crowd dynamics is complex given… (numbers, locations, patterns of obstacles), arrangement
  Need a computational simulation-based method
    We have models that simulate crowd dynamics
    Need a framework to simulate a numerically significant number of configurations
      To optimize elements in design space

## Slide 3: Crowd Behaviour
Notes:   Recent research has found that adding obstacles in crowd simulation can increase crowd flow….

## Slide 4: Motivation
Why optimize?
  Have: behaviour for environment
  Want: environment for behaviour
Simulation construction
Architectural design
Evaluate with ground truth
Crowd dynamics are complex
  Perfect steering algorithm
    If we had one we could optimize for obstacle placement
Notes: We have found that we can effect the behaviour of a crowd by adding obstacles
  The crowd simulation algorithms give a behaviour for a particular environment
  What if we could get the environment for a desired behaviour for the crowd.

## Slide 5: Related Work
Crowd Evaluation [Singh et al. 09, Kapadia et al. 11]
Crowd Optimization
  Parameters have significant effect [Pettré et al. 12, Pellegrini et al. 09, Davidich and Koester. 11, Wolinski et al. 14]
  Optimize to match reference data, objective function [Berseth et al. 14, Wolinski et al. 14]
Game Level Optimization: [Cardamone et al. 11, Sorenson and Pasquier. 10]
Architecture Optimization: [Rodriguez et al. 13]
Notes: Recent research in crowd analysis and optimization supports this work

## Slide 6: Contributions
Framework to analyze configuration space
Study local collision avoidance strategies
Optimize obstacle placement w.r.t. desired behaviour
Could put a system diagram
Notes: The contribution we make…

## Slide 7: Overview
Framework for analysing and optimizing crowd flow
Three representative steering algorithms
time
Notes: A brief overview of the work

## Slide 8: A Scenario
A scenario s = <O,A>
  Set of Obstacles O
  Set of Agents A
Each agent a A and obstacle o O has
  Position, x
  Geometry {square, circular}
Agents also have target locations
Notes: We start by defining a Scenario

## Slide 9: Parameterized Scenario
Define subspace of scenarios
Agent regions
  Bounding area to place number of agents (blue box)
  Locations can be randomly sampled
  Collective target location (Green circle)
Optimization regions
  Bounding region where obstacles can be located (grey box)
Scenario parameters p
  Determine number and location of obstacles
Notes: Next, we construct a parameterized scenario this is a looser definition of a scenario. That we call a scenario subspace

## Slide 10: Crowd Flow
ta, the completion time for agent a
|A|, number of agents in scenario
|Ac|, number of agents that complete scenario
Notes: The behaviour we are interested in studying is crowd flow

## Slide 11: Steering Algorithms
ORCA [van den Berg et al. 11]
PPR [Singh et al. 09]
Social Forces [Helbing et al. 2000]
Notes: We use 3 steering algorithms, chosen because they are very representative of the different steering models.

## Slide 12: One-way Hallway Benchmark
Example Subspace
Randomly sampled crowd
Goal Region for crowd A
  Avoids congestion
Region to optimize obstacle placement
Notes: Regions are important, don’t use goal location

## Slide 13: Path Planning Issues
Grid-based planning
Discontinuities
Crowd Congestion
Dilute effects of steering strategy
Don’t use planning
Uniform Sampling of Optimization Region
low
high
Blue is better
Notes: The first thing you might think of to do is a uniform, brute force sampling of the optimization region, for a single obstacle…
We found that global navigation was causing issue in crowd flow behaviour
Explain the graph in the middle

## Slide 14: Uniform Sampling of Optimization Region
Significant difference between algorithms
Obstacle geometry
  ORCA preferred square; SF, circular
PPR
SF
ORCA
Notes: After we stop using global navigation methods we get a nice smooth crowd flow behaviour with respect to the location of a singe obstacle
Single Obstacle
  Sampled at 2.5cm
Repulsive forces between sf agents and ROUND obstacles are smoother

## Slide 15: Obstacle Optimization
Optimize for multiple obstacles
Need obstacle overlap penalty
Objective
Non-convex function
Notes: Now that we have a smooth function for crowd flow…

## Slide 16: CMA-ES optimization
Handles noise
Works well with non-convex functions
Competitive convergence speed
Easy to implement and use
Competitive convergence speed
Easy to implement and use
Example optimization
Notes: To handle non-convex optimization…
Move picture

## Slide 17: More Benchmarks
Two-way Egress
Bi-directional Hallway
Four-way Hallway
Notes: I’ll briefly descried the other benchmarks we used…

## Slide 18: Uni-directional Hallway
2.19
1.92

## Slide 19: Bi-directional Hallway
Flow: 3.63
Flow: 2.84
Notes: Form lanes of traffic

## Slide 20: Four-way Hallway
Flow: 3.48
Flow: 3.93
Notes: Circular behaviour in the crowd

## Slide 21: Discussion
Overall the optimal number of pillars is 3
Optimization convergence:
  Fastest for Uni-directional
  Slowest for Egress
Adding pillars increases flow
Pillar arrangement
  Placed in parallel with crowd flow (Uni or Bi)
  Triangular pattern in Egress and Four-way
Notes: After optimizing on a collection of benchmarks over a set of crowd simulation algorithms…

## Slide 22: Doorway width analysis
Notes: We are also interested in studying the effect of doorway with on the behaviour of the crowd and the optimal locations of pillars.
Play the video

## Slide 23: Doorway width Analysis
Related to flow
Large increase for Egress
More important for perpendicular crowd flow
Flow dependant on door arrangement
Doorway width
Notes: We find that..
Doorway width is related to flow
  Increasing….
Significant improvement for Egress benchmark
These results show that flow is dependant on doorway arrangement
We find it is more important to increase door width for perpendicular crowd flow

## Slide 24: Review
Obstacle number and placement important
Doorway width is important
Limitations:
  Optimal obstacle placement different for algorithms
  Need for community to establish real algorithm
Future work
  More steering algorithms
  Global Navigation
Notes: Obstacle number and placement significant
Doorway width
Optimal placement can be dependant on steering algorithm
  Need a perfectly human algorithm
Expand work to more steering algorithms

## Slide 25: Questions?
Environment Optimization for
Crowd Evacuation
By
Glen Berseth1, Muhammad Usman2, Brandon Haworth2, Mubbasir Kapadia3, Petros Faloutsos2
University of British Columbia1, York University2, Rutgers University3